# SCORCHER DISTRIBUTOR

### OWNER INFORMATION

PLEASE READ CAREFULLY AND RETAIN FOR FUTURE SERVICING REQUIREMENTS

#### SPECIFICATION

MODEL	4850 SC

SUGG. STATIC TIMING	14  deg. B.T.D.C.

Timing requirements may vary depending on engine specifications,

fuels and operating conditions

POINTS GAP	.4 to .5 mm.  (.015 to .019)

DWELL ANGLE	48 to 52  deg.

REPLACEMENT PARTS

CAP	GB 820	/	9 231 065 507

ROTOR	GB 787	/	1 234 332 231

POINTS	GB 700	/	1 237 013 121

CONDENSOR	GB 824	/	9 231 067 347

Most Scorcher Distributors are derived from popular Bosch

components which are readily available from Bosch

spare parts stockists or your Scorcher dealer.

#### DISTRIBUTOR CARE

Apply high melting point grease to contact rubbing block and

a smear of grease to distributor cam when replacing points.

Apply one or two drops of oil to the felt under the rotor at each

service.

When removing rotor, lever gently at the base to avoid dislodging

the cam retaining clip.