MGA & MGB

## COIL-OVER FRONT & INDEPENDENT REAR

# SUSPENSION KITS

GENERAL:

Designed and developed by Gerry Hawkridge of Hawk Cars and John Hoyle former owner of NG Cars, both highly respected specialist car manufacturers producing Cobra replicas and thirties style roadsters based on MGB components.

These front and rear kits have been designed for easy fitting and maintain the track dimensions. No cutting of the bodywork or chassis is required and the original components could easily be re-fitted at a later date.

All parts are manufactured from good quality materials to very high standards, powder coating or plating being employed throughout. Every last nut & bolt is included in the kit.

Each telescopic suspension unit is adjustable for ride height and damping, is factory tested, and comes with its own performance report and 2 year warranty. For those who want a softer or firmer ride optional springs are available.

FRONT:

Kit consists of upper & lower tubular wishbones (with ‘dial-in’ camber adjustment and shims for caster adjustment), coil-over shock absorbers, top turret, rose jointed anti-roll bar links, and all fittings and fixings.

The existing lower wishbone pivots and stub axles are retained, while the cross member requires a minor modification by cutting and welding (or a powder coated pre-modified one can be supplied)

Both top and bottom wishbones can be fitted with standard MGB rubber, V8 metalastic, polyurethane, or nylatron bushes (8 required).

REAR:

Consists of a differential subframe and tiebars (8 bolt fixing) that carries the upper and lower tubular wishbones (shimmed for camber and tracking adjustment), coil-over shock absorbers, and machined alloy hub carriers. The kit also includes stainless steel braided brake hoses, handbrake cables, polyurethane wishbone bushes, and all fittings and fixings.

Other mechanical parts are sourced from the Ford Granada, Scorpio, and Sierra ranges. Differentials with various ratios and limited slip option, half shafts (need shortening or supplied), CV joints, hub assembly, drive flanges (Ford + splined adapter for centre lock or special version supplied for bolt-on wheels with MGB stud pattern), brake discs and callipers. All these Ford parts can be supplied.

NB: Rear Suspension Units can be supplied fully built ready for bolting to your car. The weight of the complete assembly is almost the same as the existing set up, the unsprung weight however is some 55 kilos less.